SCHEDULE 7 TO clause 37.04 CAPITAL CITY ZONE

Shown on the planning scheme map as CCZ7.

Melbourne arts precinct

Purpose

To strengthen the Melbourne Arts Precinct as an arts cultural and creative industry precinct of State significance.

To support the growth of arts, cultural and creative industry uses such as media, digital screen, design, writing and publishing, literature, fashion, performing arts, digital games development, broadcasting, music, cultural heritage and arts education and craft.

To facilitate arts, cultural and creative industry uses within the first four storeys of a building by providing appropriate spaces such as performance space, rehearsal space, galleries, workshops, event spaces and studios.

To ensure that the design of buildings deliver street frontage activation, design excellence and contributes to the legibility of the Melbourne Arts Precinct.

To provide for commercial and residential uses above the first four storeys of a buildings.

1.0	Table of uses

Section 1 - Permit not required

| Use | Condition |
| --- | --- |
| Accommodation (other than Corrective institution) | Must not be located within the first four storeys of a building except for part of a building which provides access such as a lobby or entrance. Any frontage at ground floor level must not exceed 2 metres. |
| Art and craft centre Child care centre Cinema based entertainment facility Dancing school Education centre Home based occupation Informal outdoor recreation Market |  |
| Food and drink premises (other than Hotel and Tavern) | The leasable floor area must not exceed 250 square metres |
| Office | Associated with arts, cultural and creative industry uses. Office use not associated with arts, cultural and creative industry uses must not be located within the first four storeys of a building. Any frontage at ground floor level to the tenancy must not exceed 2 metres. |
| Place of assembly (other than Amusement parlour, Nightclub and Restricted place of assembly) |  |
| Place of worship | The gross floor are of buildings must not exceed 250 square metres |
| Postal agency Railway station Tramway |  |
| Shop (other than Adult sex bookshop, Department Store and Restricted retail premises) | The leasable floor area must not exceed 200 square metres |
| Any other use not in Section 3 | Must be conducted by or on behalf of Melbourne Parks and Waterways or Parks Victoria under the Water Industry Act 1994, the Water Act 1989, the Marine Act, the Port of Melbourne Authority Act 1958, the Parks Victoria Act 1998 or the Crown Land (Reserves) Act 1978. |
| Any use listed in Clause 62.01 | Must meet the requirements of Clause 62.01 |

Section 2 - Permit required

| Use | Condition |
| --- | --- |
| Adult sex product shop Amusement parlour |  |
| Car park | Must meet the requirements of Clause 52.06. |
| Corrective institution Department store Hotel |  |
| Industry | Must not be a purpose listed in the table to Clause 53.10. |
| Leisure and recreation (other than Dancing school and Informal outdoor recreation) Nightclub Restricted place of assembly Tavern Utility installation Warehouse (other than Freezing and cool storage, and Liquid fuel depot) |  |
| Any other use not in Section 1 or 3 |  |

Section 3 - Prohibited

Use

Freezing and cool storage Liquid fuel depot

2.0	Use of land

Application requirements

The following application requirements apply to an application for a permit under Clause 37.04, in addition to those specified in Clause 37.04 and elsewhere in the planning scheme and must accompany an application, as appropriate, to the satisfaction of the responsible authority:

The description of the proposed use  and the types of activities which will be carried out.

The compatability of the proposed use with the purpose of the zone.

The likely effects, if any, on nearby uses and residential amenity including noise levels, traffic, parking, the hours of delivery and dispatch of goods and material, hours of operation, light spill, solar and glare.

An application for a residential use must be accompanied by an acoustic assessment to the satisfaction of the responsible authority, which addresses:

The likely noise source to impact the development.

The maximum permissible noise from nearby noise sources.

The necessary measures to attenuate these noise impacts, including how the proposal will meet the following requirements:

Habitable rooms of new dwellings adjacent to high levels of external noise shoul be designed to limit internal noise levels to a maximum of 45dB Lacq, in accordance with the relevant Australian Standards for acoustic control.

Exemption from notice and review

An application for the use of land is exempt from the notice requirements of Section 52(1)(a), (b) and (d), the decision requirements of Section 64(1), (2) and (3) and the review rights of Section 82(1) of the Act.

Referral of applications

An application for use of the first four storeys of a building must be referred in accordance with sections 55 of the Act to the referral authority specified in the schedule to Clause 66.04.

Decision guidelines

The following decision guidelines apply to an application for a permit under Clause 37.04, in addition to those specified in Clause 37.04 and elsewhere in the scheme which must be considered, as appropriate, by the responsible authority:

The compatibility of the proposed use with the purpose of this schedule.

The compatibility of the proposed use with any existing uses within the same building or on adjoining and nearby land.

The extent to whether the proposed use serves or supports arts, cultural and creative industry uses.

The extent of arts, cultural and creative industry floor spaces relative to the height and overall floor space of the building.

3.0	Subdivision

Exemption from notice and review

An application to subdivide land is exempt from the notice requirements of section 52(1)(a), (b) and (d), the decision requirements of section 64(1), (2) and (3) and the review rights of section 82(1) of the Act.

4.0	Buildings and works

Permit Requirement

No permit  is required to construct a building or construct or carry out works for the following:

Buildings or works carried out by or on behalf of Melbourne Parks and Waterways or Parks Victoria under the Water Industry Act 1994, the Water Act 1989, the Marine Act, the Port of Melbourne Authority Act 1958, the Parks Victoria Act 1998 or the Crown Land (Reserves) Act 1978.

Buildings or works for Railway purposes.

Alterations to a building authorised under the Heritage Act, provided the works do not alter the existing building envelope or floor area.

Footpath vehicle crossovers provided they are constructed to the satisfaction of the responsible authority.

Bus and tram shelters required for public purposes by or for the Crown or a public authority in accordance with plans and siting to the satisfaction of the responsible authority.

Decorations, gardens and planting required for public purposes by or for the Crown, a public authority or the City of Melbourne.

A work of art, statue, fountain or similar civic works required for public purposes by or for the Crown, a public authority or the City of Melbourne.

Buildings or works or uses on public land for which a current permit exists under a City of Melbourne local law.

The erection of information booths and kiosks required for public purposes by or for the Crown, a public authority or the City of Melbourne.

Traffic control works required by or for the Crown, a public authority or the City of Melbourne.

The construction, or modification, of a waste pipe, flue, vent, duct, exhaust fan, air conditioning plant, lift motor room, skylight, security camera, street heater or similar minor works provided they are to the satisfaction of the responsible authority.

A modification to the shop front window or entranceway of a building to the satisfaction of the responsible authority having regard to the architectural character of the building.

An addition or modification to a verandah, awning, sunblind or canopy of a building to the satisfaction of the responsible authority.

The painting, plastering and external finishing of a building or works to the satisfaction of the responsible authority.

Changes to glazing of existing windows to not more than 15% reflectivity.

External works to provide disabled access that complies with all legislative requirements to the satisfaction of the responsible authority.

A permit is required to demolish or remove a building or works. This does not apply to:

- Demolition or removal of temporary structures.

- Demolition ordered or undertaken by the responsible authority in accordance with the relevant legislation and/or local law.

Before deciding on an application to demolish or remove a building, the responsible authority may require an agreement pursuant to Section 173 of the Planning and Environment Act 1987 between the landowner and the responsible authority requiring, as appropriate:

- Temporary works on the vacant site should it remain vacant for 6 months after completion of the demolition.

- Temporary works on the vacant site where demolition or construction activity has ceased for 6 months, or an aggregate of 6 months, after commencement of the construction.

Temporary works must be constructed to the satisfaction of the responsible authority.

Temporary works may include:

- The construction of temporary buildings for short-term retail or commercial use. Such structures shall include the provision of an active street frontage.

- Landscaping of the site for the purpose of public recreation and open space.

Application Requirements

The following application requirements apply to an application for a permit under Clause 37.04, in addition to thise specified in Clause 37.04, and elsewhere in the scheme and must accompany an application, as appropriate, to the satisfaction of the responsible authority:

- An application for a permit must be accompanied by a written urban context report documenting the key planning influences on the development and how it relates to its surroundings.  The urban context report must identify the development opportunities and constraints, and document the effect of the development, as appropriate, in terms of:

The compatibility of the proposed development with the purpose of this schedule.

Built form and character of adjacent and nearby buildings.

Heritage character of adjacent and nearby heritage places.

Microclimate, including sunlight, daylight and wind effects on streets and other public spaces.

Energy efficiency and waste management.

Ground floor street frontages, including visual impacts and pedestrian safety.

Public infrastructure, including reticulated services, traffic and car parking impact.

Vistas

The intended arts, cultural and creative industry uses, including the floor area and any specifications or requirments.

An application to construct a building or to construct or carry out works must include as appropriate, upgrading of adjacent footpaths or laneways to the satisfaction of the responsible authority.

An application for a permit to construct or carry out works for development of a building listed in the Heritage Overlay must be accompanied by a conservation analysis and management plan in accordance with the principles of the Australian ICOMOS Charter for the Conservation of Places of Cultural Significance 1992 (The Burra Charter) to the satisfaction of the responsible authority.

An application to construct a building or construct or carry out works for a residential or other noise sensitive use, must be accompanied by an Acoustic Assessment to the satisfaction of the responsible authority, which addresses:

- The likely noise sources to impact the proposed development.

- The maximum permissible noise from nearby noise sources.

- The necessary measures to attenuate these noise impacts, including how the proposal will meet the following requirement:

  - Habitable rooms of new dwellings adjacent to high levels of external noise should be designed to limit internal noise levels to a maximum of 45dB Laeq, in accordance with the relevant Australian Standards for acoustic control.

An application to construct podium carparking must:

- Locate car parking on the first floor or above.

- Sleeve car parking at street frontages with suitably designed floorspace including sufficient depth for the nominated  arts, cultural and creative industry use.

Exemption from notice and review

An application to construct a building or construct or carry out works for a use in Section 1 of Clause 37.04-1 is exempt from the notice requirements of section 52(1)(a), (b) and (d), the decision requirements of section 64(1), (2) and (3) and the review rights of section 82(1) of the Act.

An application to demolish or remove a building or works is exempt from the notice requirements of section 52(1)(a), (b) and (d), the decision requirements of section 64(1), (2) and (3) and the review rights of section 82(1) of the Act.

Referral Requirement

An application for development with a gross floor area exceeding 25,000 square metres must be referred in accordance with section 55 of the Act to the referral authority specified in the schedule to Clause 66.04.

An application for development of the first four storeys of a building must be referred in accordance with section 55 of the Act to the referral authority specified in the schedule to Clause 66.04.

Decision guidelines

The following decision guidelines apply to an application for a permit under Clause 37.04, in addition to those specified in Clause 37.04 and elsewhere in the scheme which must be considered, as appropriate, by the responsible authority:

The purpose of this schedule.

The views of the Office of the Victorian Government Architect as appropriate, as to the architectural expression and materiality of the proposal having regard to the significance of the Melbourne Arts Precinct.

The convenience of  pedestrians, bicycles and vehicle access within and through the precinct.

The impact the proposal will have on street amenity if on-site car parking occupies any of the first four floors of a building and whether any above ground car parking is sleeved by arts, cultural and creative industry or other active uses.

The adequacy of car parking provision and loading bays.

The safety and efficiency of  of vehicle entry and egress.

Whether the building is designed to accommodate arts, cultural and creative industry uses as part of the overall development and over time.

Whether the development provides adequate space and floor to ceiling heights so that it could be adapted for arts cultural and creative industry uses in the future.

Whether the building enables a a visual relationship between occupants of upper floors and pedestrians, and better surveillance of the street.

The interface between the development and the public realm including:

Whether the development contributes to the legibility of the Melbourne Arts Precinct as an arts precinct.

Whether the building design at street level provides for active street frontages, pedestrian engagement and weather protection.

The opportunities for passive surveillance of the public realm from occupants of upper storeys of the development.

The impact the proposal will have on street amenity if buildings are not constructed to the street boundary at ground level.

Whether the development would compromise the function, form and capacity of public spaces and public infrastructure.

The impact on the amenity of any dwellings on adjacent sites.

Whether the development providesacceptable internal noise levels within habitable rooms of new dwellings taking into account existing or reasonably anticipated future noise sources.

Whether the development includes appropriate measures to attenuate against noise associated with the operation of other businesses and activities, including limiting internal noise levels of new habitable rooms.

The adequacy and accessibility of waste and recycling facilities.

Whether the demolition or removal of buildings gives effect to a permit or prior approval for the redevelopment of land.

Whether the demolition or removal of buildings is required for environmental remediation of contaminated land.

The provision of temporary buildings and works or landscaping to avoid vacant sites for excessive periods.

5.0	Signs

A permit is required to construct and display a sign except for:

Advertising signs exempted by Clause 52.05-4

An under-verandah business sign if:

- It does not exceed 2.5 metres measured horizontally, 0.5 metres vertically and 0.3 metres between the faces of the sign;

- It is located between 2.7 metres and 3.5 metres above ground level and perpendicular to the building facade; and

- It does not contain any animation or intermittent lighting.

A ground floor business sign cantilevered from a building if:

- It does not exceed 0.84 metres measured horizontally, 0.61 metres vertically and 0.3 metres between the faces of the sign;

- It is located between 2.7 metres and 3.5 metres above ground level and perpendicular to the building facade; and

- It does not contain any animation or intermittent lighting.

A window display.

A non-illuminated sign on a verandah fascia, provided no part of the sign protrudes above or below the fascia.

Renewal or replacement of an existing internally illuminated business identification sign.

Exemption from notice and review

An application to construct or display a sign, is exempt from the notice requirements of section 52(1)(a), (b) and (d), the decision requirements of section 64(1), (2) and (3) and the review rights of section 82(1) of the Act.

# Text boxes

--/--/20--

Proposed C323

--/--/20--

Proposed C323

--/--/20--

Proposed C323

--/--/20--

Proposed C323

--/--/20--

Proposed C323

--/--/20--

Proposed C323